## Slide 1: Module EGE321 Wireless Communication & Networking Chapter 2 Wireless Communications System

## Slide 2: Contents
  2. Wireless Communications System
  2.1 Communication System Architecture
  2.2 Radio Propagation and Link Budget Analysis
  2.3 Digital Modulation Technique

## Slide 3
Analogue
  An analogue signal is defined as a physical time-varying quantity and is usually smooth and continuous.
Digital
  A digital signal, on the other hand, is made up of discrete symbols selected from a finite set.
...
t
Amplitude
Digital Signal
...
t
Amplitude
Analogue Signal
Fundamentals - Analog & Digital Signals
...
t
Amplitude
Analogue Signal
...
t
Amplitude
Digital Signal

## Slide 4
Digital Transceiver Architecture
Format
Multiplex
Channel
Encoder
Source
Encoder
Spread
Format
Demultiplex
Channel
Decoder
Source
Decoder
Despread
Bits or Symbol
To other
destinations
From other sources
Digital input
Digital output
Source bits
Source bits
Channel bits
Carrier & symbol
synchronization
Channel
bits
Multiple
Access
Waveforms
Multiple
Access
Tx
Rx
Performance
Measure
Modulate
Demodulate
& Detect
Input signal

## Slide 5
ADC
Sampling Function
Generator
Encoder
Sampling pulses
Analog Input Signal
t
amplitude
TS
PCM Codes
011 110 100 010...
TS = sampling interval (s)
fS= 1/TS = sampling frequency (Hz)
Process of converting Analog signal to Digital format
000
001
010
011
100
101
110
111
0
1
3
5
7
Quantized
Level
PCM Codes
1
2
3
4
VFS
q
Operation of the Analog to Digital Converter
Digital Transceiver Building Block – ADC
Digital Signal

## Slide 6
Digital signal represent by ‘0’ or ‘1’
0 or 1 that represents information to be transmitted through the communication system.
What is bit rate?
Bit rate is the number of bits that are conveyed or processed per unit of time.
Information transfer rate or Bit rate: the speed at which binary information (bits) can be transferred from source to destination.
Example: if 10 bits of information are sent every second, then
Information transfer rate = 10 bits / 1s = 10 bps (in 1 sec, 10 bits can tx)
Unit of information transfer rate : bits / second or bps
Fundamentals - Information Transfer Rate (Bit Rate)

## Slide 7: Fundamentals - Symbol Rate
What is symbol rate?
Symbol rate (baud rate or modulation rate) is the number of symbol changes, waveform changes, or signalling events, across the transmission medium per time unit using a digitally modulated signal or a line code.
Example:
If 1 bit = 1 symbol, then the symbol rate would be the same as the bit rate.
If 2 bits = 1 symbol then the symbol rate would be half of the bit rate.
Symbol rate = bit rate / the number of bits to represent a symbol.
Unit of symbol rate: Symbol / second or sps

## Slide 8
Digital Modulation Part 1. How Data Speed Works: Throughput, Bits, Baud & Channel Rate Demystified!
https://youtu.be/LkG0iXV4d2E
Pls see this Youtube video to understand more.

## Slide 9: Fundamentals – Binary Signaling
Every 1 second, 1 bit of data is send which is 1 bps
10 second, this is the data “1 1 0 1 1 0 0 1 0 0”
Bit 1
Bit 0
1 1 0 1 1 0 0 1 0 0
Open
Close
Bit rate = 1 bps
1 Symbol = 1 bit, then the symbol rate is 1 sps

## Slide 10: Fundamentals – M-ary Signaling
Every 1 second  1 bit of data is 1 bps
Every 10 second, I can send “1 1 0 1 1 0 0 1 0 0”
1 1  No one
1 0  Jenny
0 1  Andy
0 0  Paul
1 1 0 1 1 0 0 1 0 0
Received data
Start from here
1st
Symbol
2nd
Symbol
3rd
Symbol
4th
Symbol
5th
Symbol
No one
Bit rate = 1 bps
1 Symbol = 2 bit, then the symbol rate is 0.5 sps

## Slide 11: Fundamentals – Binary Signaling
In Binary Signaling: One Symbol is used to represent One bit
Symbol Rate = Bit Rate
Binary
Modulator
S1(t)
S2(t)
1 0 1
For Binary Signaling:
S1(t)
S2(t)
S1(t)
2 possible states
“1” or “0”
ASK, BPSK, FSK
K = number of bit make into a symbol
M = number of possible state = 2k
For this case
K =1
And therefore M=2

## Slide 12: Fundamentals – M-ary Signaling
For M-ary Signaling, one symbol is represented by more than 1 bit.
    Group of k bits represented by One Symbol from 2k-symbol set
Symbol Rate = Bit Rate / k = Bit Rate / log2M
M-ary
Modulator
S1(t)
S2(t)
.
.
.
SM(t)
For M-ary Signalling:
Group of k bits
01...100…00...10
M=2k symbols
MPSK, MFSK
M-QAM
To represent group of k bits, M=2k symbols are required.
K = number of bit make into a symbol
M = number of possible state = 2k
For this case
K =4
And therefore M= 24 = 16

## Slide 13: Example (1)
A mobile radio can support a symbol rate of 8kbps within a bandwidth of 20 kHz by encoding 2 bits in each symbol.
Compute the following:
The data/bit rate.
ANS
Data/Bit rate = Symbol rate x k (Given, k is 2)
= 2 x 8kbps = 16kbps
The bandwidth efficiency of the radio link.
ANS
BW efficiency = data rate / bandwidth =16k/20k = 0.8 bps/Hz

## Slide 14: Shannon Capacity Theorem
The Shannon-Hartley capacity limit for error-free communication is given by:
Channel Capacity, C = BW log2 (1 + S/N ) bps
Shannon–Hartley theorem tells the maximum rate at which information can be transmitted over a communications channel of a specified bandwidth in the presence of noise.
Fundamentals – Capacity Theorem

## Slide 15: Shannon Capacity Theorem
Example:
A telephone line has a bandwidth of 0 to 4 kHz, and the maximum signal to noise ratio (S/N) on the line is 20 dB. What is the channel capacity for error free transmission?
  BW = Highest freq – lowest freq = 4kHz
  C = BW log2(1+S/N)
  Therefore C = (4000-0) log2(1+1020/10)
= 4000 log2(101)
= 26.63kbps
Fundamentals – Capacity Theorem

## Slide 16
Digital Transceiver Architecture
Format
Multiplex
Channel
Encoder
Source
Encoder
Spread
Format
Demultiplex
Channel
Decoder
Source
Decoder
Despread
Bits or Symbol
To other
destinations
From other sources
Digital input
Digital output
Source bits
Source bits
Channel bits
Carrier & symbol
synchronization
Channel
bits
Multiple
Access
Waveforms
Multiple
Access
Tx
Rx
Performance
Measure
Modulate
Demodulate
& Detect
Input signal

## Slide 17
Input signal
The source of information can be analog / digital, e.g. analog: audio or video signal, digital: like teletype signal. In digital communication the signal produced by this source is converted into digital signal consists of 1′s & 0′s.
Source Encoder
In digital communication we convert signal from source into digital signal as mentioned above. The point to remember is we should like to use as few binary digits as possible to represent the signal. In such a way this efficient representation of the source output results in little or no redundancy. This sequence of binary digits is called information sequence.
Source Encoding or Data Compression: the process of efficiently converting the output of wither analog or digital source into a sequence of binary digits.
Digital Transceiver Building Block

## Slide 18
Channel Encoder
The purpose of the channel encoder is to introduce some redundancy in the binary information sequence that can be used at the receiver to overcome the effects of noise and interference encountered in the transmission on the signal through the channel.
Digital Modulator
The binary sequence is passed to digital modulator which in turns convert the sequence into electric signals so that it can transmit on channel. The digital modulator maps the binary sequences into signal wave forms, for example if we represent 1 by sin x and 0 by cos x then we will transmit sin x for 1 and cos x for 0.
Digital Transceiver Building Block

## Slide 19
Communication Channel
The communication channel is the physical medium that is used for transmitting signals from transmitter to receiver. In wireless system, this channel consists of atmosphere, for traditional telephony, this channel is wired, there are optical channels, under water acoustic channels etc.
Digital Demodulator
The digital demodulator processes the channel corrupted transmitted waveform and reduces the waveform to the sequence of numbers that represents estimates of the transmitted data symbols.
Digital Transceiver Building Blocks

## Slide 20
Channel Decoder
This sequence of numbers then passed through the channel decoder which attempts to reconstruct the original information sequence from the knowledge of the code used by the channel encoder and the redundancy contained in the received data
Source Decoder
At the end, if an analog signal is desired then source decoder tries to decode the sequence from the knowledge of the encoding algorithm. And which results in the approximate replica of the input at the transmitter end.
Output Transducer
Finally we get the desired signal in desired format analog or digital.
Digital Transceiver Building Blocks

## Slide 21
The Roles of Source Encoder, Channel Encoder & Encryption of a Transmitter of Digital Transceiver.
https://youtu.be/ymF3ZMlp4f8
Pls see this Youtube video to understand more.

## Slide 22
Digital Transceiver: Roles of Modulator (ASK, FSK & PSK). Draw the Time Diagram of ASK, FSK & PSK.
https://youtu.be/EzkrhXHouNg
Pls see this Youtube video to understand more.

## Slide 23
Example1:
What is function of the source coding in a digital transmitter?
ANS
The function of the source coding is to perform data compression of the input source to achieve a minimal representation of the input waveform.
Example2:
What is the function of the channel encoder in a digital transmitter?
ANS
Channel encoder is to combat channel impairments by adding redundancy bits for error detection and correction.
Digital Transceiver Building Block

## Slide 24
Information source and input transducer
Source encoder
Channel encoder
Digital modulator
& Upconverter
Source decoder
Channel decoder
Digital demodulator
& Downconverter
Basic elements of a digital communication system
e.g. speech source & A-to-D conversion of speech
removes redundancy, e.g. speech compression
adds redundancy (e.g. linear block codes, cyclic codes & convolutional codes) to combat channel impairment
baseband filtering, data formatting based on modulation scheme (BPSK, QPSK), upconversion, power amplification, etc
Output Transducer
propagation loss, shadowing, multipath, etc
Encryption
security of information
Decryption
Digital Transceiver Building Block
Transmitter
Receiver
Propagation
Media

## Slide 25
Digital Transceiver Building Block
Encryption & Decryption
Encryption is the process of translating plain text data (plaintext) into something that appears to be random and meaningless (ciphertext).
Decryption is the process of converting ciphertext back to plaintext. To encrypt more than a small amount of data, symmetric encryption is used.

## Slide 26
  1. Random errors : occur randomly in the received sequence.
    mainly due to thermal noise, also called Gaussian noise.
    codes designed to correct random errors are called random-error-correcting codes, e.g. Block Codes & Convolutional Codes
  2. Burst errors : occurs in clusters of message in the received sequence.
    mainly caused by multipath fading.
    burst errors can be corrected using a combination of random-error correcting codes & time interleaving
  3. Diffuse Errors : combination of burst & random errors
    Can be corrected using concatenated codes, example: random-error-correcting codes + Reed-Solomon Codes.
Digital Transceiver Building Block – Channel Coding
Types of errors

## Slide 27
Thank you