## Slide 1: Module EGE321 Wireless Communication & Networking Chapter 2.2 Radio Propagation and Link Budget
  2.2 Radio Propagation and Link Budget

## Slide 2: Contents
  2.2 Radio Propagation and Link Budget
  2.2.1 Electromagnetic Wave Propagation
  2.2.2 Propagation Path Loss Model
  2.2.3 Link Performance Analysis
  2.2 Radio Propagation and Link Budget

## Slide 3
Electromagnetic Wave Propagation
Radio Propagation Model – EIRP
Tx
PT = 1 W
Lf = 1 dB
GT = 30 dB
EIRP
  2.2 Radio Propagation and Link Budget
Effective, or Equivalent, Isotropically Radiated Power (EIRP) is the maximum amount of power that could be radiated from an antenna, given its antenna gain and the transmitter power of the RF system. EIRP is most commonly given in dB or dBm.
The diagram shows the location of EIRP and the equations to compute the EIRP is as following:
  EIRP = PTGT (watts)
  EIRP (dBm) = PT (dBm) + GT (dB)

## Slide 4
Example
Calculate the EIRP of a microwave transmitting installation where the transmitter output power is 1 W, the total feeder cable loss is 1 dB, and the transmitting antenna gain is 30dB.
Electromagnetic Wave Propagation
Radio Propagation Model – EIRP
Tx
PT = 1 W
Lf = 1 dB
GT = 30 dB
EIRP
ANS
EIRP (dBm) = PT (dBm) –Lf (dB) + GT (dB)
= 10 log (1W/0.001W) – 1 dB + 30 dB
= 30 dBm – 1 dB + 30 dB
= 59 dBm
  2.2 Radio Propagation and Link Budget

## Slide 5
What is Link Budget & How to Calculate the Link Budget to Estimate the Quality of Comm Link.
https://youtu.be/y35j8wb0eBU
Pls see this Youtube video to understand more.

## Slide 6
Hata published an empirical formula based on Okumura's results to predict path loss, and is valid from 150 MHz to 1500 MHz
The standard formula for the path loss in urban areas is given by:
  Where f : Frequency between 150-1500 MHz
  hte : Effective height of transmitter between 30-200 m
  hre : Effective height of receiver between 1-10 m
  d : Distance between transmitter and receiver in km
  A(hre): Correction factor for mobile antenna height
For a large city we take
A(hre) = 3.2[ log(11.75 hre)]2 - 4.97 (dB) for f  300 MHz
Propagation Path Loss Models
Okumura’s Hata Model
  2.2 Radio Propagation and Link Budget

## Slide 7
A mobile subscriber that is living at a distance, d = 3500 m from a base station complained to the cellular operator that his mobile phone reception is not very good. You are asked to investigate to find out the problems and make the necessary recommendations. Details are as follows:
Frequency of operation, f : 935.2 MHz
Base Station transmitted output power, PT : 20 W
Base Station transmitter antenna gain, GT : 10 dB
Base Station transmitter antenna height, hte : 50 metre
Mobile Station receiver sensitivity, PR : -100 dBm
Mobile Station receiver antenna gain, GR : 3 dB
Mobile Station receiver antenna height, hre : 1.6 metre
Assume that all other losses are negligible except for the path loss, using Okumura-Hata propagation model and determine the path loss, LP (dB).
Propagation Path Loss Models
Okumura’s Hata Model
Example:
  2.2 Radio Propagation and Link Budget

## Slide 8
Example:
Using Okumura-Hata propagation model to determine the path loss.
A­ (hre) = 3.2 [log (11.75hre)]2 - 4.97 (dB)
= 3.2 [log(11.75 x 1.6)]2 - 4.97
= 0.2251
LP = 69.55 + 26.16 log f(MHz) – 13.82 log hte – A(hre) + [44.9 – 6.55 log hte] [log d (km)]
= 69.55 + 26.16 log(935.2) - 13.82 log(50) - 0.2251 + [44.9 - 6.55 log 50] log3.5
= 141.94 dB
Propagation Path Loss Models
Okumura’s Hata Model
  2.2 Radio Propagation and Link Budget

## Slide 9
Transmitter
Power
Amplifier
Receiver
Transmit Power
PT (dBm)
Feeder cable
Transmit Antenna
Receive Antenna
Received Power
PR (dBm)
Path Loss PL (dB) and
Fade Margin FM (dB)
Gain GR (dB)
Cable loss
Lf (dB)
Feeder cable
Gain GT (dB)
Cable loss
Lf (dB)
Propagation Path Loss Models
Link Performance Analysis
  2.2 Radio Propagation and Link Budget
Communication link includes the entire communication path from the information source, through the transmitter, RF channel and receiver up to the information sink

## Slide 10
By examining the link budget, we can determine whether communication system meets the requirements comfortably or marginally or fail to meet the specifications
A link analysis consist of calculating the useful signal power and the interfering noise power available at the receiver. The output of the link analysis is a link budget which shows the gains and losses
Some link budget parameters are statistical such as allowances for fading. Therefore the link budget is an estimation technique for evaluating the communication system performance
Propagation Path Loss Models
Link Performance Analysis
  2.2 Radio Propagation and Link Budget
Link budget enough?

## Slide 11
Bit Error Rate (BER) is used in digital system to measure the quality of the demodulator output in terms of the number of bits wrongly decoded
  BER = total bits received in error/total bits transmitted
Signal to Noise Ratio (SNR)
  The SNR is a measure of performance at the various points of a communication link
  SNR (dB) =10 log ( signal power/noise power)
  The SNR can be degraded (lowered) through
    The decrease of the desired signal power
    The increase of noise power (noise) or interfering signals (interferences)
Propagation Path Loss Models
Link Performance Analysis – Performance Criteria
  2.2 Radio Propagation and Link Budget

## Slide 12
Link budget accounts for the total losses and gains in a transmission link from transmitter output to the receiver SNR at the input to the demodulator
Radio link design of a mobile communication system generally involves the tradeoff among the following 3 parameters (factors):
  Transmit power (PT)
  Propagation path loss (LP)
  Receive Power (PR) or Rx sensitivity
Propagation Path Loss Models
Link Performance Analysis – Radio Link Design
  2.2 Radio Propagation and Link Budget

## Slide 13
To guarantee detection at the Receiver, we must have:
  PT(dBm) + (Gains)dB – (Losses)dB  PR (dBm)
  where
  PT = transmit power
  Gain = transmit and receive antenna gain
  Losses = total losses at the antenna feeder loss, filter and circulator loss, propagation path loss, fade margin, etc
  PR = Rx sensitivity for a specified SNR or BER. This is the minimum signal strength that must be received at the receiver antenna in order to guarantee a certain level of performance at the receiver output
    For analog link SNR is normally 12dB SINAD.
    For mobile digital link, the BER could be 1x10-6
  Fade Margin
  Refers to the margin in dB that has to added to the path loss to account for multipath fading
Propagation Path Loss Models
Link Performance Analysis – Radio Link Budget
  2.2 Radio Propagation and Link Budget

## Slide 14
Consider a particular base station in a cellular system operating in a large city with the following parameters :
Frequency of operation: 915 MHz
Base transmitter output power, Pt: PT ( to be determined )
Mobile receiver sensitivity, Pr: -113 dBm
Base transmitter antenna gain, Gt: 6 dB
Mobile receiver antenna gain, Gr: 3 dB
Height of base transmitter, hte: 50 m
Height of mobile receiver, hre: 2 m
Assuming all other losses are negligible except path loss and Rayleigh fading. Provision for fade margin for 99.8% reliability may be calculated with the help of the Rayleigh distribution chart provided (Treat the Fade Margin as additional loss along the path)
Propagation Path Loss Models
Link Performance Analysis – Radio Link Example
  2.2 Radio Propagation and Link Budget

## Slide 15
Transmitter
Power
Amplifier
Transmit Power
PT (dBm)
Receiver
Received Power
PR (dBm)
Path Loss PL (dB) and
Fade Margin FM (dB)
Receive Antenna
Gain GR (dB)
Feeder cable
Cable loss
Lf (dB)
Transmit Antenna
Gain GT (dB)
Feeder cable
Cable loss
Lf (dB)
Propagation Path Loss Models
Link Performance Analysis – Radio Link Example
  2.2 Radio Propagation and Link Budget

## Slide 16
i) Write down the system equation.
Pt – Lf + Gt – Lp - FM + GR – Lf = PR
Given that feeder losses are negligible, Lf = 0
Pt + Gt – Lp - FM + GR = PR
ii) Given that a cell radius of 3 km is required, calculate the path loss.
A(hre) = 3.2[ log(11.75 hre)]2 - 4.97
= 3.2[log(11.75 x 2)]2 - 4.97
= 1.045 dB
PL = 69.55 + 26.16log f - 13.82log hte - A(hre) +
(44.9 - 6.55log hte )(log d)
= 69.55 + 26.16log(915) – 13.82log(50) – 1.045 +
(44.9 – 6.55log(50))log(3)
= 138.14 dB
Propagation Path Loss Models
Link Performance Analysis – Radio Link Example
  2.2 Radio Propagation and Link Budget

## Slide 17
iii) Determine the required power of the transmitter, PT with 99.8% of communication link.
From the Rayleigh distribution chart (99.8% reliability):
Propagation Path Loss Models
Link Performance Analysis – Radio Link Example
  2.2 Radio Propagation and Link Budget
25 dB

## Slide 18
iii) Pt – Lf + Gt – Lp - FM + GR – Lf = PR
Transmit power required Pt = PR + Lf - Gt + Lp + FM - GR + Lf
= -113 + 0 – 6 + 138.14 + 25 - 3 + 0
= 41.14 dBm
With transmit power of 41.14 dBm, we can be sure that the receiver will have the probability of 99.8% of receiving the signal.
Propagation Path Loss Models
Link Performance Analysis – Radio Link Example
  2.2 Radio Propagation and Link Budget

## Slide 19
Parameters | Values (dB)
Tx power(dBm) | 45
Antenna cable loss | 3
Tx Antenna Gain (dBi) | 13
EIRP(dBm) (= 45 – 3 + 13) | 55
Path Loss | 150
Fade Margin(dB) | 0
Other margin components(dB) such as building penetration loss | 0
Received isotropic power(dBm) (= 55 – 150 – 0 - 0) | -95
Rx Antenna Gain (dBi) | 4
Mobile antenna cable loss (dB) | 1
Rx signal power (dBm) (= -95 + 4 – 1) | -92
Rx noise power kTB (dBm) | -126
Rx CNR(dB) (= -92 – (-126)) | 34
Target Rx CNR(dB) | 13
Margin(dB) (= 34 – 13) | 21
Propagation Path Loss Models
Link Performance Analysis – Radio Link Example
  2.2 Radio Propagation and Link Budget

## Slide 20
How to Calculate the Required Link Budget to Establish a Communication Link with a Case Study.
https://youtu.be/meb4a5oeTDA
Pls see this Youtube video to understand more.

## Slide 21
Model | Formula
Free Space Propagation Model | LP (dB) = 32.44 + 20 log d (km) + 20 log f (MHz)
Okumura’s Hata Model | A­ (hre) = 3.2 [log (11.75hre)]2 - 4.97 (dB) LP = 69.55 + 26.16 log f(MHz) – 13.82 log hte – A(hre) + [44.9 – 6.55 log hte] [log d (km)]
Plane Earth Model | L (dB) = 120 + 40 log dkm - 20 log[hr(m) ht(m)]
Link Budget | Pt – Lf + Gt – Lp - FM + GR – Lf = PR
Propagation Path Loss Models
Link Performance Analysis – Useful Formula
  2.2 Radio Propagation and Link Budget

## Slide 22
Homework
  2.2 Radio Propagation and Link Budget
A RF engineer is tasked to set up a base station within a cell radius d = 2 km in a new town. The operator team has provided the following parameters:
  Frequency of operation = 920 MHz
  Base Station feeder loss, LF = 2 dB
  Base station transmitting antenna gain, GT = 10 dB
  Height of Base station, hT = 40 m
  Mobile station sensitivity, PR = -113 dBm
  Mobile station receiving antenna gain, GR = 3 dB
  Height of Mobile station, hR = 2 m

## Slide 23
Homework
  2.2 Radio Propagation and Link Budget
  1) The required fade margin for 99% reliability.
  2) Write down the system equation in terms of the given parameters.
  3) The path loss, Lp, using Okumura Hata Model.
  4) The required Base station transmitter power PT.

## Slide 24
Thank you